## Slide 1: Festival of Lights
Technical Teach In
5/11/2021

## Slide 2: Agenda
Sound Systems
Jingle Bell Rock
DMX

## Slide 3: Sound Systems
https://drive.google.com/drive/folders/1v5zLXFOrcpogjYSqEk8hEICQRdYDcKUj?usp=sharing

## Slide 4: Hardware
Arduino Nano
DFPlayer Mini
TF/Micro SD card
5v regulator
1k resistor
Breadboard

## Slide 5: Bill of Materials
Qty Reqd | Description | Supplier | Unit cost | Total cost
1 | KOOKYE 5PCS Nano V3.0 ATMEGA328P Module CH340G 5V 16M Mini USB Micro-controller Board for Arduino(Nano5) | Amazon | $3.80 | $3.80
1 | 4GB MicroSDHC Memory Card | Amazon | $8.00 | $8.00
1 | 12VDC 1A Wall Adapter Power Supply | Amazon | $4.89 | $4.89
1 | 1K Ohm 1/8 Watt 1% Metal Film Resistor | Amazon | $0.11 | $0.11
1 | Hook and Loop Tape Roll Self Adhesive Strips Sticky Back Fastener, 1In wide Black | Amazon | $0.12 | $0.12
1 | L7805CV Positive Voltage Regulator Output 5v TO-220 Package | Amazon | $0.35 | $0.35
1 | DAOKI U Disk Mini MP3 DFPlayer Player Module Audio Voice Board | Amazon | $3.20 | $3.20
1 | HAMMOND 1591CSBK ENCLOSURE, MULTIPURPOSE, ABS, BLACK | Amazon | $6.72 | $6.72
1 | Premium Dual 1/4 Inch To Dual RCA Audio Cable (3FT) - Male 6.35mm 1/4" Phono Mono to RCA Connector Wire Cord Plug Jack | Amazon | $7.99 | $7.99
2 | Metal Panel Mount RCA Female Socket Connectors Adapter 20 Pcs Silver Tone | Amazon | $0.41 | $0.82
1 | 70mm x 90mm Welding Soldering Copper Strip Prototype PCB Printed Circuit Board Stripboard | Amazon | $1.00 | $1.00
1 | SINNRY 10 Pcs 5.5mm x 2.1mm DC Power Socket Female Threaded Mount Connector Adapter | Amazon | $1.40 | $1.40
 |  |  | Total | $36.99

## Slide 6: Circuit Design
Audio Out

## Slide 7: Software

## Slide 8: Theory of operation
MP3 file stored on TF Card/Micro SD
TF Card inserted into DFPlayer Mini
Arduino Nano
  Initializes DFPlayer Mini music player using serial interface
  Waits until DFPlayer Mini is Not Busy
  Then restarts music using serial interface
Notes:
  Single MP3 file
  Box runs on 12v ; Regulated to 5v for Arduino; 1k resistor used to limit Tx

## Slide 9: Music
All music must be in MP3 format
All music files stored at https://drive.google.com/drive/folders/1YRBtsyW5Qj3rGyeWWWs9fnZrS2q31ibl?usp=sharing
Just copy file to TF/Micro SD card (rename as necessary)

## Slide 10: Jingle Bell Rock
https://drive.google.com/drive/folders/0B4cAR8jE9SuCeWpMb0tjUXBMV1E?usp=sharing

## Slide 11: Jingle Bell Rock
Hardware
Software
Lighting
  Boxes
  Overheads
Pneumatics

## Slide 12: Hardware
Display is 12 columns and 8 rows
Each column is driven by a single custom driver board
Overall control is from single Arduino board

## Slide 13: Custom Driver Board

## Slide 14: Board Layout
All CAD is in Eagle
All files are at https://drive.google.com/drive/folders/17efMtp1bh-j9D9nAtmnYIbDMgi13Wgm8?usp=sharing

## Slide 15: Theory of Operation
Each PCB has 8 open collector outputs that drive the LEDs (8 Channel IC TLC59211)
Each of the cells in the display boards has LEDs that are connected to Vcc
To illuminate the LED, the open collector output is driven low
Each PCB has an 8 bit serial shift register
Data is fed to the board from Arduino using a single data pin and a single clock pin
Each of the driver boards is daisy chained so that each bit of data is pushed all the way down all shift registers

## Slide 16: Software
All code is at https://drive.google.com/drive/folders/1uBSZQX1YDXt6i-stIYo7uj-wT9Z7c_Lm?usp=sharing
All software runs on Arduino

## Slide 17: Software Notes
On Startup
  Initialize all data and array lights
  Test the total array to show pixels stuck ON or OFF
Cycling
  Text Messages
  Christmas trees
  Snowflakes
  Drizzle
Cycling for static parade
  Assorted additional text messages

## Slide 18: Things to note in software
The display is mimic’d with an software internal array; the whole array is then pushed to the physical display
Bits must be pushed as rapidly as possible to reduce flicker
Functions are available to scroll Left, Right, Up and Down
Characters are “drawn” using a dot matrix character set – static data in program
FOL_LED_19.ino is the latest version

## Slide 19: Lighting
Box Lighting
  Cheap DMX lights triggered to change color based on sound input
  Could be configured to change color under control on DMX Controller
Overhead lighting
  Higher quality Chauvet lights
  Set to maximum brightness
  Could be configured to change color under control on DMX Controller

## Slide 20: Pneumatics
Ron is the specialist
Valves are currently controlled from timed relays inside float
Timed Relays connected to valves using ribbon cable
Notes
  Lighting driver board was designed to be able to drive relays if needed. Pinouts for ribbon cable matches 

## Slide 21: DMX Ideas

## Slide 22: DMX Concepts
DMX is the standard for lighting and sound control for theatrical and stage systems
DMX 512 is wired standard that uses 3 or 5 pin XLR connectors
E1.31 is new wireless standard

## Slide 23: Potential Lighting solutions
Use Vixen Lights on PC to create schedule/program of synchronized music, lights and motion
Download program to Falcon Player running on Raspberry Pi
Use Falcon/Raspberry Pi to control
  Our DMX 512 lights through a serial to DMX converter
  E1.31 lighting strands wirelessly using ESPixel Pops
  Our DMX 512 lights through a proprietary E1.31 converter
  Pneumatic Motion through a serial to GPIO to driver board
Note: I have had a prototype version of this already working

## Slide 24
Par
Light
192.168.0.9
CN
Light
DMX
3 Pin
Arduino Mega
Falcon Player
DMX
3 Pin
Router
GPIO
Raspberry Pi 4 Model B
Falcon Player
DMX Shield
TTY AMA0
TXD GPIO14
Pneu
Act
20v
Serial1
GPIO
Laptop PC
Vixen Lights
Pneu Driver Bd
Revision 2.0
Serial0
Serial2
115200
Rx1
16 channel
Relay Board
DMX

## Slide 25
Par
Light
192.168.0.9
CN
Light
DMX
3 Pin
Arduino Mega
Falcon Player
DMX
3 Pin
Router
GPIO
Raspberry Pi 4 Model B
Falcon Player
DMX Shield
TTY AMA0
TXD GPIO14
Pneu
Act
20v
Serial1
GPIO
Laptop PC
Vixen Lights
Pneu Driver Bd
Revision 2.0b
Serial0
Serial2
115200
Rx1

## Slide 30
Figure 1
Solenoid a
Solenoid b
Solenoid c
Solenoid d
Connector
DMX Relay Board
Figure 2
Solenoid a
Solenoid b
Solenoid c
Solenoid d
Connector
Figure 3
Solenoid a
Solenoid b
Solenoid c
Solenoid d
Connector
Figure 4
Solenoid a
Solenoid b
Solenoid c
Solenoid d
Driver
Sequencer
L4
L5
L3
L2
L1
20v
DMX
DMX Interface
Amplifier
Falcon
Raspberry Pi
Vixen
PC Laptop